Describe Block 17 - NFT Features here.
Previous version
Block 17 - NFT Features-V2.0
== Intro ==
We are expecting the following levels of tiling.
Image Number
GSD of last image
Pre-tile Now
Post-Recon A
Post-Recon B
Area
1-11
8cm
14cm
NA
NA
Global'ish
11-17
5cm
5cm
NA
NA
Several 100m
18-23
3.4cm
5cm
NA
NA
100x100m TAG
Check Point
23-26
2.3cm
5cm
2cm
NA
50x50m TAG
Match Point
27-29
0.6cm
5cm
2cm
1cm
25x25m TAG

## General

## Setup
Extra item names
- A 15cm DEM for evaluation
- B... and following
- Z is a single maplet over the region (22cm/Q=49)
- Y is the tiling bigmap (22cm/Q=116)
- X is the matching maplet that provides extra "umph" to the 35cm images (22cm/Q=81 - just a touch bigger)
- W is the working maplet.
  We use this for all of our processing.
  A is a published version and not the starting thing.
- V is a small bitmap that just covers the ROI
bigmap	Q	GSD	Width	Purpose
A...	67	15cm	20m	10m radius, published to the team
B, C...	200	5cm	20m	10m radius, published to the team
V	60	5cm	6m	Just barely covers the ROI, assuming 6m radius
W	350	5cm	35m	Baseline width we use for the ROI to cover outlying regions
X	99	5cm	10m	Central reference maplet. Used to denote the middle of the object for lithos, CSPLOT, etc
Y	250	5cm	35cm	The region to tile at 14 and 5cm
Z	49	5cm	5m	Temporary maplet, used in evaluation scripts -- dynamically built.

Tiling using XXXXXY, <idY>. Iterate over XXXXX, <idA>