# Block 6B - Bigmap Tiling Lunar

## Description
This block is used to tile the surface with high-resolution, bigmap-referenced landmarks.

## Procedure
For bigmaps with a Q less than 1000, use standard procedures Block 6B - Bigmap Tiling v2
For bigmaps with a Q greater than 1000, break up the bigmap into a larger number of bigmaps that are all less than Q=1000.

### Example
For Q=1100, make 5 IN files
Tile03m.IN
m<center of ROI>49 490.00338 1100 1.23400 1000TIL03S1.005.025111111100
Tile03m01.IN
mTIL03S <----- Reference the above map550 5500.00338 550 1.23400 1000TIL0311.005.025111111100
Tile03m02.IN
mTIL03S1650 5500.00338 550 1.23400 1000TIL0321.005.025111111100
Etc...