# Block 6B - Bigmap Tiling

#### This is version 0 - as of 23 Feb 2016

## Description
This block tiles a bigmap with a new suite of landmarks. Bigmap and maplet parameters are specified by the user, using the bigmap in files contained in /SPC_Test/F3-base/base/support/ and the lithos options contained in the seed files in /SPC_Test/F3-base/base/scripts/.

## Assumptions
- You have invoked a Bourne-Again Shell (bash) on ormacsrv1.lpl.arizona.edu
- You have completed the processing steps in Block 1 - Setup Directory V0
- You have set up the test sub-directory following the steps in Block 0
- You have ingested and registered test images following the steps in:
  - Block 2
  - Block 3

## User inputs
- bigmapName - Name of bigmap .in file located in /SPC_Test/Working/lsupport/ (for example, 'TILE20.in')
- GSD - Maplet Ground Sample Distance in km (for example, '0.0002')

## Procedure

### 1. Initial Inputs

# User inputs:GSD=0.00020bigmapName=TILE20

### 2. Set-up

# Set-Upcd /SPC_Test/$testID/test/scriptdatepwdls -lls -l /usr/local/binrm LMRKLIST1.TXT # Empties the list of new landmarks

### 3. Make tiling bigmap

# Make tiling bigmapecho "Bigmap .in file: support/$bigmapName.in"cat lsupport/$bigmapName.inls -l /usr/local/bin/bigmapbigmap < lsupport/$bigmapName.in

### 4. Check resulting file

# check resulting file## Tiling bigmap has the same name as the .in file, ## i.e. TILE20.in, produces the tiling bigmap: TILE20echo $bigmapName | showmapconvert $bigmapName.pgm ~/send/$bigmapName.jpg

### 5. Setup tiling

# Set up tiling/bin/cp -f MAPFILES/$bigmapName.MAP MAPFILES/XXXXXX.MAPls -l /usr/local/bin/map_coverageecho "XXXXXX" > map_coverage.inecho 0 >> map_coverage.inecho $GSD >> map_coverage.inmap_coverage < map_coverage.inconvert coverage_m.pgm ~/send/$bigmapName-beforeTiling.jpgecho "N" | make_tilefile | tee make_tilefile.outsed 1d make_tilefile.out > temp.outecho "XXXXXX" > make_scriptT.inecho "scripts/$GSD.seed" >> make_scriptT.incat temp.out >> make_scriptT.in cat make_scriptT.inmake_scriptTls -l

### 6. Invoke tiling script

# Invoke tiling scriptcat INIT_LITHOS.TXTlithos -vnohup sh run_script.b &

### 7. Monitor progress

# Monitor progressls -l *.INN *.OOTfind_nofitTsh support/logEvalP.sh

### 8. Clean directory

# Clean directorysh rem_script.brm TESTFILES/*rm TESTFILES1/*

### 9. Complete procedure

# Block Completeexit# Save block logmv typescript typescript-$bigmapName

(Compiled by DL)
CategoryHowTos