## DN2TEMP.TXT
Category B	Version 3.0.1

### Description
This input file contains the parameters to convert DN values (level 0 images) into temperatures and the weighting to apply to the final solution.

### Coefficients
- Cameras 1, 2, 3 do not use the coefficients.
- Cameras 4 and 5 (TAGCAMs) use only the first two.
- Coefficients 3 and 4 are never used.
The camera's thermoresister is calculated as
T_i = DN * C13 + DN * C22 + DN * C3 + C4

### Weighting
There are four thermoresisters on each camera. The weights 1-4 provide how much impact each thermoresistor should have. While this example has it totaling 1.0, SPC normalizes the weighting, so it isn't needed.
- N = W1 + W2 + W3 + W4
- T_final = T1 * W1/N + T2 * W2/N + T3 * W3/N + T4 * W4/N

### Columns
Camera Number	Coef 1	Coef 2	Coef 3	Coef 4	Weight 1	Weight 2	Weight 3	Weight 4
	C1	C 2	C 3	C 4	W 1	W 2	W 3	W 4

Here is a sample DN2TEMP.TXT file:

1 0.80168E+02 -0.69285E-01 0.23237E-04 -0.37331E-08 0.25 0.25 0.25 0.252 0.80168E+02 -0.69285E-01 0.23237E-04 -0.37331E-08 0.25 0.25 0.25 0.253 0.80168E+02 -0.69285E-01 0.23237E-04 -0.37331E-08 0.25 0.25 0.25 0.254 -263.15 0.15259 0 0 1.D0 0.D0 0.D0 0.D05 -263.15 0.15259 0 0 1.D0 0.D0 0.D0 0.D0C NAV & NFT CAMERA HEAD TEMPERATURE PARAMETERS FROMC UA-SIS-9.4.4-322_OSIRIS-REx-NavCam-Data-Product-SIS_Rev_2.0_CCv0005.pdfCC OCAMS CAMERA HEAD TEMPERATURE PARAMETERS CALCULATED FROMC OREX-DOC-05.01-00259_OCAMS Flight SW Engineering Dictionary_Rev_C_CCv0018.pdfC Fit to DN 1200 - 3400 (TC from ~ 25 to -35) has RMS = 0.18C, MAXDEV = 0.30CC Focal length temperatures for OCAMS are linear combinations of housekeeping temperatures:C TMC = F1*MCFWHTMP+F2*MCFWMTMP+F3*MCLENTMP+F4*MCROETMPC TSC = F1*SCFWHTMP+F2*SCFWMTMP+F3*SCLENTMP+F4*SCROETMPC TPC = F1*PCFOHTMP+F2*PCFOMTMP+F3*PCMR1TMP+F4*PCROETMPC

 CategoryThreeOhOne