# Find normal
(lithos Main Menu Option N. Find normal )

## Description
This Main Menu option calculates the normal vector to the maplet in one of several ways.

### Suboptions
When you choose Option N. Find normal from the Main Menu, you will see this set of Suboptions:

Main Menu: Q 0123O IUCRSG NVAMBX DEPL FZH? n >n 1. Normal from radius vector 2. Normal from heights 3. Normal from shape 4. Normal from stereo q. Quit
1. Normal from radius vector - Sets normal the same as the radius vector. (Rarely used.)
/!\ Note that the normal is the same as the radius vector everywhere if the object is a sphere. Rarely will conditions on an asteroid be such that this option will be correct.
2. Normal from heights - Determines normal from the average of the heights in the maplet by fitting a plane to the current topography. (Used almost exclusively.)
3. Normal from shape - Determines normal from the shape model.
4. Normal from stereo - Determines normal from three common points in two images.
/!\ This option is occasionally used when the shape is extremely challenging and no good model yet exists. It requires manual determination of common points.

## Typical Example
The following sample shows the command input for the most common suboption choice, '2':
n2

(Compiled by JRW)
CategoryLithosMenu