# How To Build A Landmark

### Objectives
- First we will generate a maplet with the following parameters:
  - center at -10, 350 (lat,wlon)
  - scale = .001 km/px
  - size:
    Q=49, width=99 x 99 px
  - name = ‘START5’

### LITHOS: Create New Landmark
- lithos
- c - create new landmark name
- START5 - landmark name
- l - define landmark control point by specifying a latitude and longitude on the body
- -10 350 - lat, lon
- .001,49 - enter scale (km/px), qsz

### LITHOS:Input the new landmark
Once the landmark is created, you need to "load" it into active memory. You use the lithos command "i" from its main menu.
- i - input landmark
- START5 - landmark name (as previously named)
- y - check for images?
- 0.5 - fractional width. (This is almost always used)
- n - reject invisibles
In a second terminal, review the LMRK_DISPLAY1.pgm image. You can use ImageMagick's "Display" command, Graphics Converter, or if using a Mac, pgm files can be displayed in the Finder or Preview.
  cd <working dir> ls -lt | head display LMRK_DISPLAY1.pgm
You can also use the SPC_Tools: landmarks

### LITHOS: Eliminate Pictures from Landmark
- e - eliminate pictures from landmark
- n - auto-eliminate new images only (a for auto-eleiminate)
- 0,50,.6,.6,0,4 - Input INVLIM,SLIM,CLIM,ILIM,RSMN,RSMX
  - 0 is typical.
    If you have objects that are obscuring the maplet, then this becomes important
  - 50 is the emission angle that we keep
  - .6 means the image must fill at least 60% of the frame
  - .6 means the illuminated service must fill at least 60% of the frame
  - 0 is minimum resolution -- almost always is 0
  - 4 is the maximum resolution ratio (how many times bigger are the image pixels than the GSD.
    3 or 4 is typical.
    6+ is seldom effective)
- INVLIM = 1000 * MAX INVISIBLE FRACTION (0-1000)
- SLIM = MAX EMISSION ANGLE (0-90)
- CLIM = MIN FRACTION OF VISIBLE (0-1)
- ILIM = MIN FRACTION IN SHADOW (0-1)
- RSMN = MIN IMGSCALE/MAPSCALE (0-inf)
- RSMX = MAX IMGSCALE/MAPSCALE (0-inf) =>set according to printout and LMRK_DISPLAY
- Most permissible: 1000,90,0,0,0,inf => does not throw any image away
- Least permissible: 0,0,1,1,inf,0 => throws all away
- display LMRK_DISPLAY1.pgm

### LITHOS: Get Heights from Shape and Find Normal, V
- m - get heights from shape model
- n - find normal
- 2 - normal from heights
- m - get heights from shape model
- u - update landmark file (save)
- 1 - save map
In 2nd terminal:
  cd Bennu ls -lt | head display LMRK_Display1.pgm more LMRKLIST.TXT more LMKFILES/START5.LMK more MAPFILES/START5.MAP showmap START5
Then display the START5.pgm (xv, imageMagick, convert, GraphicConverter)

### LITHOS: Align Landmarks in Pictures
Option 1. Use this when the template you see in LMRK_DISPLAY1.pgm is poor	Option 2 (typical). Use this as much as you can
1 - align landmarks	1 - align landmarks
3 - align with picture	0 - align with template
23 - picture #2 in LMRK_DISPLAY	3 - enter spacing
1 - enter spacing	n - new spacing?
y - new spacing? Yes b/c it only aligned a few images	0 - continue
2 - enter spacing	y - update landmark pixel locations?
y - new spacing? Yes b/c it only aligned a few images	1 - align landmarks
3 - enter spacing	0 - align with template
y - new spacing? Yes b/c 3 caused a couple images to shift>10px	1 - enter spacing
2 - enter spacing	n - new spacing?
n - new spacing? No, lets just use the correlated images first	0 - continue
0 - continue	y - update landmark pixel locations?
y - update landmark pixel locations?
1 - align landmarks
3 - align with picture
1 - picture #2 from last iteration became picture #1
1 - enter spacing
n - new spacing?
0 - continue
y - update landmark pixel locations?

display LMRK_Display1.pgm

### LITHOS: Find Template
- u - update landmark file (save)
- 1 - Save map
- 0 - find template
- c - use correlated
- .5 - enter correlation limit
- 0 - find template
- 0 - continue
- 44 - number of iterations
display LMRK_Display.pgm

### LITHOS: Align Landmarks and Find Template
- 1 - align landmarks
- 0 - auto align
- 1 - enter spacing
- y - new spacing?
- 2 - enter spacing
- n - new spacing?
- 0 - continue
- y - update landmark pixel locations?
- 1 - align landmarks
- 0 - auto align
- 1 - enter spacing
- n - new spacing?
- 0 - continue
- y - update landmark pixel locations?
display LMRK_Display1.pgm
- 0 - find template
- c - use correlated
- .5 - enter correlation limit
- 0 - find template
- 0 - continue
- 44 - number of iterations
display LMRK_DISPLAY1.pgm
REPEAT ONCE

### LITHOS: Solve for Heights
- 2 - find heights
- 8 - fill with shape
- 2 - include existing heights
- .01 - input fraction of points
- 1 - auto include neighboring maps
- 4 - include limb vectors
- 1,2.5,3 - input expansion, res/scale limit, d_hgt limit
- 6 - include differential stereo
- y - use gradients?
- y - autoheights?
- 0 - begin iteration
- .025 - input weight
- 30 - enter number of iterations
- 0 - end iterations
display LMRK_DISPLAY1.pgm display slope.pgm

### LITHOS: Final Alignment and Save
- 1 - align landmarks
- 0 - auto align
- 1 - enter spacing
- n - new spacing?
- 0 - continue
- y - update landmark pixel locations?
- # We are skipping V-4 fo