# ISIS to Emission
NOTE: We generate the emission data first since this shell script first initializes the LROC NAC EDR, which will be used by incidence and I/F.
The shell script here generates phoE.IMG.

# 4 Aug 2017 - Eric E. Palmer# Script to do many of the steps required for building a photometric cube# Requires a lot of directory setup.# Calibrated images in working/NEW_IMAGES# EDR images in img-<last4)[LR]# Modified by JRW Oct 6 2017# Modified by JRW Aug 28 2018# Modified by JRW Nov 19 2018 to include last five digits.# Usage# gen.sh <calibratedIMG> <last5[LR]>file=$1out=$2if [ '$file' == '' ]then echo "Usage $0 <calibratedIMG> <last5L>"fiif [ '$out' == '' ]then echo "Usage $0 <calibratedIMG> <last5L>"fiecho "File: $file"echo "Outfile: $out"if [ 'two' == 'two' ]then lronac2isis FROM=$file.IMG TO=$file.cub spiceinit FROM=$file.cub shape=ellipsoid caminfo FROM=$file.cub TO=info.txt # Generate emission data phocube FROM=$file.cub TO=phoE-$out.cub I=false PHASE=false LAT=false LON=false isis2pds FROM=phoE-$out.cub to=phoE-$out.img BITTYPE=u16bit STRETCH=linear MINPER=0 MAXPER=100ficalFile=`echo $file | tr E C`echo "calFile: $calFile"# Create an image that is really the image's phase#ln -s ../working/NEW_IMAGES orig#../bin/mergePhase $calFile emiss.img#mv M*C.IMG orig# Get the directory ready for dumpMapLRO.f#ln -s ../working/MAPFILES .
Generating the IMG takes awhile, so we have a wrapper to run all the images at once. NOTE: This wrapper requires directory setup. Each image is placed in its own folder; the folder name is the last 5 digits of the NAC, plus the L or R for left/right. The wrapper should be placed in the directory containing all the image folders.

# 5 Aug 2018 - John Weiric2# Wrapper for ISISe.sh to run multiple files# Usage# sh wrapperISISe.sh <imageList># Modified Nov 19 2018 to include last 5 digits.file=$1list=`cat $file`for i in $listdo# need to determine the last five characters since# that is how the directories are set up strLength=`echo $i | wc | cut -c23-24` if [ "$strLength" != "13" ] then if [ "$strLength" != "14" ] then echo "string length not supported" exit fi fi if [ "$strLength" == "13" ] then lastFive=`echo $i | cut -c6-11` echo $lastFive fi if [ "$strLength" == "14" ] then lastFive=`echo $i | cut -c7-12` echo $lastFive fi#exit# with last five character, can now get into folder cd img-$lastFive ../ISISe.sh $i $lastFive cd ..done
- With the emission IMG in hand, now attach the original image header. The source code is found here. mergeEmission.c
- Below is a wrapper to run the "merge" software.

# 20 Nov 2018 - John Weirich# Wrapper for t.mergeEmission to run multiple files# Usage# sh wrapperMergeEmission.sh <imageList>file=$1list=`cat $file`cd /Users/JW/LDAP16/IMG_RG2for i in $listdo# need to determine the last five characters since# that is how the directories are set up strLength=`echo $i | wc | cut -c23-24` if [ "$strLength" != "13" ] then if [ "$strLength" != "14" ] then echo "string length not supported" exit fi fi if [ "$strLength" == "13" ] then lastFive=`echo $i | cut -c6-11` echo $lastFive fi if [ "$strLength" == "14" ] then lastFive=`echo $i | cut -c7-12` echo $lastFive fi#exit# with last five character, can now get into folderecho "$i.IMG" > emmTmpecho "/Users/JW/LDAP16/CubesReinerGamma2/img-$lastFive/phoE-$lastFive.img" >> emmTmp~/Dropbox/Ingenii/src/t.mergeEmission < emmTmp\mv -f ME* /Users/JW/LDAP16/CubesReinerGamma2/working/NEW_IMAGES/donerm emmTmp