# Imager_Grid
Category D	Version 3.0

## Description
imager_Grid makes images from a the shape model.

## Setup
To make images you'll first need the following directories/files in your working directory:
Directories:
- SUMFILES/
  - Filled (you'll need to copy these files or generate new ones)
- SHAPEFILES/
  - Filled
Files:
If running manually, no files other than the directories above are needed.

## Execution

 input 12-character picture nameP596409118A3 Input alternate shapefile? (y/n)ySHAPEFILES/shapeSPC_75Draft.v5d-64 gc TEMPFILE.pgm Raw file = P596409118A3.DAT
1. Enter the image name that is stored in SUMFILES.
2. Which shape do you want to use?
3. To use SHAPE.TXT, enter "n"
4. To use a different shape, enter "y" and give the path from the working directory. i.e. SHAPEFILES/MYSHAPE

## Output
The resulting DAT file will be placed in the working directory. In the example above that is P596409118A3.DAT. To generate many images, you'll want to make a wrapper, and have that wrapper move all the DAT files into IMAGEFILES. All DAT files can be viewed by running "viewImages.sh" obtained from EEP.

 Compiled by JW