# MAKE_TILES
Category B	Version 3.0

## Description
This program builds <sequence>.IN files that are used to make Z-maps with bigmapL. Z-maps are essentially a combination of bigmaps that, together, fully wrap around the shape model.
MAKE_TILES creates a <sequence>.IN file for every row in the input file MAPLIST.TXT.
/!\ Be sure to include enough bigmap names to fully wrap around the surface (calculate with q-size and surface area of shape).

### Required Files
MAPLIST.TXT - List of bigmap names you want to use.

### Output Files
<sequence>.IN files - One for each row in MAPLIST.TXT

## Using MAKE_TILES
The standard input includes these elements:
- resolution (pix/km)
- Q size
- seed
- maximum maplet resolution that can be included in the bigmap being created
Here is a sample input:

0.02500 500 1.23400 5.00000
Here is a sample MAPLIST.TXT file:

ZN0000ZN0001ZN0002ZN0003ZN0004ZN0005ZN0006ZN0007ZN0008ZN0009ZN0010ZN0011END
The following is a sample sequence.in file created from the above inputs:

l 0 0 0.02500 500 1.23400 5.00000ZN00001.005.025111111100

(Compiled by KD)
CategoryPrograms