# Normalized Cross-Correlation Evaluation
This page describes the methodology for using normalized cross-correlation to evaluate a region of the model.
Cross-correlation is performed on the following images:
- Model: Image of bigmap
- Truth: Image of Zmaps
Model (left), Truth (right), S/C Azimuth 0, Zenith 30deg, Sun Azimuth 90deg, Zenith 45deg:
Images are generated using the following set of dirty sumfiles at the required resolution to include:
- low and high phase
- low and moderate incidence
- full set of s/c azimuth angles (observe region from all directions).
Spacecraft		Sun
Azimuth (deg)	Zenith (deg)	Azimuth (deg)	Zenith (deg)
0	30	90	45
90	30	90	45
180	30	90	45
270	30	90	45
0	30	270	45
90	30	270	45
180	30	270	45
270	30	270	45
45	10	270	10

Image resolution is chosen from the following based on the state of the model:
Resolution: 120cm, 75cm, 35cm, 18cm, 9cm, 5cm.
The following regions have been identified for evaluation:
Region ID	Region Name	Latitude (deg)	West Longitude (deg)	Description
TG	TAG Site 1	-10	350	Shape 4 TAG site 1
R1	Region 1	45	300	Region of roughness, identified from a visual inspection using Small Body Mapping Tool

## Where are the Dirty Sumfiles and Truth Images?
SUMFILES: ormacsrv1:/opt/local/spc/shape4/imageGen/DIRTYSUMFILES/
 Truth .pgm files: ormacsrv1:/opt/local/spc/shape4/imageGen/PGMFILES/
Follow this link for details of the image file and bigmap naming conventions: Normalized Cross-Correlation Evaluation - Naming Conventions

## Obtain Model Bigmap
Obtain the required bigmap/s from the model working directory (or back-up). A full set of bigmap .in files is stored here:
/opt/local/spc/shape4/support4/MR1051_model_REG1_GSD5cm_width100m.inMR1052_model_REG1_GSD5cm_width20m.inMR1055_model_REG1_GSD5cm_width50m.inMR1101_model_REG1_GSD10cm_width100m.inMR1102_model_REG1_GSD10cm_width20m.inMR1105_model_REG1_GSD10cm_width50m.inMR1351_model_REG1_GSD35cm_width100m.inMR1352_model_REG1_GSD35cm_width20m.inMR1355_model_REG1_GSD35cm_width50m.inMTG051_model_TAG1_GSD5cm_width100m.inMTG052_model_TAG1_GSD5cm_width20m.inMTG055_model_TAG1_GSD5cm_width50m.inMTG101_model_TAG1_GSD10cm_width100m.inMTG102_model_TAG1_GSD10cm_width20m.inMTG105_model_TAG1_GSD10cm_width50m.inMTG351_model_TAG1_GSD35cm_width100m.inMTG352_model_TAG1_GSD35cm_width20m.inMTG355_model_TAG1_GSD35cm_width50m.in

## Populate Evaluation Directory
The F6 evaluation directory is here:
/Volumes/Data1/spc-test/F6-evaluation/drwxrwxr-x 227 dlambert OREX\spc 7718 Jul 22 15:09 DIRTYNOMINALSdrwxrwxr-x 227 dlambert OREX\spc 7718 Jul 22 15:09 DIRTYSUMFILESdrwxrwxr-x 226 dlambert OREX\spc 7684 Jul 21 16:01 SUMFILESdrwxrwx--x 13 jweirich OREX\spc 442 Jul 21 14:38 eval_F6_BBD1_TGdrwxrwx--x 15 jweirich OREX\spc 510 Jul 21 14:34 eval_F6_EndApp_TGdrwxrwxr-x 14 dlambert OREX\spc 476 Jul 20 16:36 eval_F6_startdrwxr-xr-x 13 dlambert OREX\spc 442 Jul 22 15:17 eval_F6_template-rw-r--r-- 1 dlambert OREX\spc 117 Jul 22 15:42 listSUM_R1_120cm-rw-r--r-- 1 dlambert OREX\spc 117 Jul 22 15:42 listSUM_R1_18cm-rw-r--r-- 1 dlambert OREX\spc 117 Jul 22 15:42 listSUM_R1_35cm-rw-r--r-- 1 dlambert OREX\spc 117 Jul 22 15:42 listSUM_R1_5cm-rw-r--r-- 1 dlambert OREX\spc 117 Jul 22 15:42 listSUM_R1_75cm-rw-r--r-- 1 dlambert OREX\spc 117 Jul 22 15:42 listSUM_R1_9cm-rw-r--r-- 1 dlambert OREX\spc 117 Jul 20 16:21 listSUM_TG_120cm-rw-r--r-- 1 dlambert OREX\spc 117 Jul 20 16:22 listSUM_TG_18cm-rw-r--r-- 1 dlambert OREX\spc 117 Jul 20 16:21 listSUM_TG_35cm-rw-r--r-- 1 dlambert OREX\spc 117 Jul 20 16:22 listSUM_TG_5cm-rw-r--r-- 1 dlambert OREX\spc 117 Jul 20 16:21 listSUM_TG_75cm-rw-r--r-- 1 dlambert OREX\spc 117 Jul 20 16:22 listSUM_TG_9cmdrwxrwxr-x 4 dlambert OREX\spc 136 Jun 24 16:16 lsupport-rw-r--r-- 1 jweirich OREX\spc 587 Jul 21 14:49 parseXcorr.sh-rw-rw-r-- 1 dlambert OREX\spc 1927 Jun 23 15:12 processing.loglrwxr-xr-x 1 dlambert OREX\spc 30 Jun 24 12:27 support -> /opt/local/spc/shape4/support4lrwxr-xr-x 1 dlambert OREX\spc 39 Jun 24 16:54 truth_PGMFILES -> /opt/local/spc/shape4/imageGen/PGMFILES
Make a subdirectory and populate as follows:
- listSUM -> ../listSUM_35cm - symbolic link to list of dirty sumfiles;
- lsupport -> ../lsupport/ - symbolic link to main directory local support directory;
- MAPFILES/ - directory containing model bigmap/s;
- MAPLIST.TXT - file listing the bigmap to image, appended with 'END';
- PGMFILES/ - directory for storage of generated .pgm files;
- SUMFILES/ - directory for storage and retrieval of SUMFILES which will be generated for the evaluation;
- THUMBNAILS/ - directory for storage of generated .jpg files;
- imageXcorr_results/ - directory for storage of imXcor.py output files;
- truth_PGMFILES -> /opt/local/spc/shape4/imageGen/PGMFILES/ - symbolic link to truth images.

dirID=eval_F6_start # Update this ID!!cd /Volumes/Data1/spc-test/F6-evaluation/mkdir $dirIDcd /Volumes/Data1/spc-test/F6-evaluation/$dirIDmkdir MAPFILES PGMFILES SUMFILES THUMBNAILS imageXcorr_resultsln -s ../lsupport .ln -s /opt/local/spc/shape4/imageGen/PGMFILES truth_PGMFILESln -s ../listSUM_TG_35cm listSUMprintf "%s\n%s\n" "MTG105" "END" > MAPLIST.TXT
Make SUMFILES which will have a unique name for the evaluated model state:
modelStateID=AA # Update this ID!!while read name; do echo $name newNmPart1=`echo $name | cut -c1-8` newNmPart2=$modelStateID newNmPart3=`echo $name | cut -c11-12` newNm=`echo ${newNmPart1}${newNmPart2}${newNmPart3}` sed 's/'$name'/'$newNm'/g' ../SUMFILES/${name}.SUM > SUMFILES/${newNm}.SUM done < listSUM

## Generate Model Images
The following script has been written to automate the generation of images of a bigmap using imager_MG. It expects the user to identify an existing list of dirty sumfiles as a common line item, e.g.:

sh lsupport/makeImages_imagerMG.sh listSUM
where

cat listSUMPBF6TG3E0001PBF6TG3E0002PBF6TG3E0003PBF6TG3E0004PBF6TG3E0005PBF6TG3E0006PBF6TG3E0007PBF6TG3E0008PBF6TG3E0009
Generate thumbnails for visual inspection of the bigmap images:
while read name; do echo $name /opt/local/bin/convert PGMFILES/${name}_MTG105.pgm THUMBNAILS/${name}_MTG105.jpgdone < listSUM

## Conduct Normalized Cross-Correlation
Conduct cross-correlation using Tanner's script, storing the output in the imageXcorr_results directory:

Mapname=MTG105while read name; do echo $name truthNM=`echo $name | sed 's/PB/P2/g'` python /opt/local/spc/bin/imXcorr.py PGMFILES/${name}_${Mapname}.pgm truth_PGMFILES/${truthNM}.pgm | tee imageXcorr_results/imXcor_${name}_${Mapname}.outdone < listSUM
Algorithm Source: J.P. Lewis
- Fast_normalized_cross-correlation.pdf
- vi95_lewis.pdf