# Stereo Angle

### By TC

## Description
This process details the usage of stereo.py, a python script loosely based on Mambo_5 meant to offer support for multiple landmarks at once without plots. This script will take a list of landmarks, and for each landmark in the list, calculate the average and maximum stereo and sun divergent angles.
**N.B. This script requires access to LMKFILES/, SUMFILES/, and an up-to-date MAPINFO.TXT. As such, residuals should be run before invocation, and the script should be run from your SPC working directory.

## Usage
For a general usage overview, run:

python stereo.py -h
Using the above command will print out the usage header:

# USAGE: python stereo.py [-option] outfile infile## -o Use this followed by 'outfile' to# specify a unique output destination.# Default is stereo.txt## -h Use this to print usage directions# to StdOut. (Prints this header)## -v Use this to only output current# version number and exit. By default# the version will be sent to StdOut# at the begining of each use.## ** N.B. If 'infile' is not specified, LMRKLIST.TXT# will be used.#######################################################
A typical invocation of this script is:

python stereo.py /path/to/maplist.txt
Using the "-o outfile" option is not necessary and is only used if you wish to specify the name and path of the outputted text file. By default the output will be stereo.txt (example shown in Output section).
If you do not specify an input file on the command line, LMRKLIST.TXT will be used by default. The input file should be a single column of 6 character landmark names, which can either have or not have "END" as the last line of the file.
Do to the potential of long processing time for landmarks with lots of images, a display of the current landmark and its position out of the total number to be processed is printed to the screen.

Working on:...EE0043 17 out of 64EE0044 18 out of 64EE0045 19 out of 64EE0046 20 out of 64EE0047 21 out of 64EE0048 22 out of 64EE0049 23 out of 64EE0050 24 out of 64...

## Output
Every time this script is run, the version and I/O files are printed to the screen for traceability.

Stereo.py version: 2.0List of landmarks used: maplistOutput file: stereo.txt
The only important output of the script is a text file (either stereo.txt or specified by -o filename.txt) which has 8 columns.
- Column 1: Landmark name
- Column 2: Latitude
- Column 3: W Longitude
- Column 4: Number of images in landmark
- Column 5: Average stereo angle between images (degrees)
- Column 6: Maximum stereo angle between images (degrees)
- Column 7: Average Sun divergent angle for landmark (degrees)
- Column 8: Maximum Sun divergent angle for landmark (degrees)

EE0027 -3.0993 267.7872 10 41.256 113.414 51.013 159.354EE0028 -3.0954 266.3576 10 54.339 108.951 66.309 145.871EE0029 -3.0966 264.9467 9 31.525 86.908 60.394 145.871EE0030 -3.0563 263.5016 14 41.796 101.030 46.626 143.882EE0031 -3.0162 262.0543 11 14.587 40.611 33.476 145.871EE0032 -2.9929 260.6454 9 13.858 40.154 35.715 145.871EE0033 -4.5369 267.7770 7 48.634 108.598 60.286 145.871EE0034 -4.5254 266.3470 6 55.354 101.181 64.559 145.184EE0035 -4.5302 264.9462 7 53.497 108.972 66.345 143.882EE0036 -4.5150 263.5352 9 52.412 108.990 67.037 145.871