# Test F3F-Photometric Function - Test Procedure here

## Directory Set-up and Image Ingest
Test F3F Procedures Block-1A - TEST DIRECTORY SET-UP - ORIG
 log: log-typescript-Block-1A-TestDirSetUp-Orig
Test F3F Procedures Block 8A - GEOMETRY/RESIDUALS
 Clean start model and perform geometry log: log-typescript-Block-8A-ResidualsGeometry-NONE-startModel
Test F3F Procedures Block-2A - INGEST IMAGES - TEST-SPECIFIC
 Block conducted on images - generic to F3F tests:
- /SPC_Test/F3-source/G2-DS-MapCam - perturbed;
- /SPC_Test/F3-source/H2-DS-PolyCam-Nadir - perturbed;
- /SPC_Test/F3-source/H3-DS-PolyCam-Stereo-v5 - perturbed.
log: log-typescript-Block-2A-IngestImages-TestSpecific
Test F3F Procedures Block-3A - REGISTER IMAGES - BATCH
 Block conducted on all DS images which fall within a 100m x 100m region centered on TAG site 1:
- 85 DS MapCam images;
- 22 DS PolyCam Nadir images;
- 35 DS PolyCam Stereo images.
Images have been pre-registered. Re-registered via make_scriptR to ensure model update and correct registration.
 log: log-typescript-Block-3A-Register-Images-F3F-DSImages
Test F3F Procedures Block-4A - AUTOREGISTER IMAGES - BATCH
 Block conducted on 85 DS MapCam images - generic to F3F tests.
 log-typescript-Block-4A-Autoregister-Images-F3F-DSMapCamImages
Model must be iterated to build topography from the new DS MapCam images however, since lithosP uses the photometric function - the iteration should be conducted at the start of each sub-test.

## Sub-Test F3F1:
Repeat the following for each sub-test.
Test F3F Procedures Block-1B - TEST DIRECTORY SET-UP - TEST
 log: log-typescript-Block-1B-TestDirSetUp-Test-F3F1
Test F3F Procedures Block-5A - ITERATE LANDMARKS Iterate 53 landmarks contained in a 100m x 100m region centered on TAG Site 1.
 log-typescript-Block-5A-Iterate-Landmarks-PostRegistrationOfDSNavCamImages
# Run residuals
 echo 5 .005 .0002 | residuals
 # Inspect lmrks
 grep ">>" RESIDUALS.TXT
 # Save residuals output files
 mkdir -p log/log-residuals-postRegistrationofDSNavCamImagesAndIteration
 cp RESIDUALS.TXT MAPINFO.TXT PICINFO.TXT RANGES_SOLVED.TXT LMKVECS.TXT log/log-residuals-postRegistrationofDSNavCamImagesAndIteration/

### 20cm Tiling
Test F3F Procedures Block-6B - TILE - BIGMAP
 16 new landmarks incorporating App, PS, and DS MapCam and PolyCam images.
 log-typescript-Block-6B-Tile-Bigmap-F3F1-TILE20
Test F3F Procedures Block-5A - ITERATE LANDMARKS
 69 landmarks to iterate
 log-typescript-Block-5A-Iterate-Landmarks-F3F1-Post20cmTiling
# Run residuals
 echo 5 .005 .0002 | residuals
 # Inspect lmrks
 grep ">>" RESIDUALS.TXT
 # Save residuals output files
 mkdir -p log/log-residuals-post20cmTilingAndIteration
 cp RESIDUALS.TXT MAPINFO.TXT PICINFO.TXT RANGES_SOLVED.TXT LMKVECS.TXT log/log-residuals-post20cmTilingAndIteration/

### 10cm Tiling
Test F3F Procedures Block-6B - TILE - BIGMAP
 64 new landmarks incorporating App, PS, and DS MapCam and PolyCam images.
 log-typescript-Block-6B-Tile-Bigmap-F3F1-TILE10
Test F3F Procedures Block-5A - ITERATE LANDMARKS
 133 landmarks to iterate
 log-typescript-Block-5A-Iterate-Landmarks-F3F1-Post10cmTiling
# Run residuals
 echo 5 .005 .0002 | residuals
 # Inspect lmrks
 grep ">>" RESIDUALS.TXT
 # Save residuals output files
 mkdir -p log/log-residuals-post10cmTilingAndIteration
 cp RESIDUALS.TXT MAPINFO.TXT PICINFO.TXT RANGES_SOLVED.TXT LMKVECS.TXT log/log-residuals-post10cmTilingAndIteration/
Test F3F Procedures Block 8A - GEOMETRY/RESIDUALS
 Run GEOMETRY, option2, to update the position of the spacecraft.
 log-typescript-Block-8A-ResidualsGeometry-F3F1-post10cmTile
Test F3F Procedures Block-5A - ITERATE LANDMARKS
 Iterate 133 landmarks contained in a 100m x 100m region centered on TAG Site 1.
 log-typescript-Block-5A-Iterate-Landmarks-F3F1-Post10cmTilingAndGeometry

### 5cm Tiling
Test F3F Procedures Block-6B - TILE - BIGMAP
 225 new landmarks incorporating PS, and DS PolyCam images.
 log-typescript-Block-6B-Tile-Bigmap-F3F1-TILE05
Test F3F Procedures Block-5A - ITERATE LANDMARKS
 Iterate 358 landmarks contained in a 100m x 100m region centered on TAG Site 1.
 log-typescript-Block-5A-Iterate-Landmarks-F3F1-Post5cmTiling

### Clean
Block 7B - Clean Bigmap
 Achieve tiled State.
 Achieve correlated state.
 Achieve imaged state.
 Achieve fitted state.
Test F3F Procedures Block 8A - GEOMETRY/RESIDUALS
 Run GEOMETRY, option2, to update the position of the spacecraft.
 log: log-typescript-Block-8A-ResidualsGeometry-F3F1-post05cmTile
Test F3F Procedures Block-5A - ITERATE LANDMARKS
 Iterate 358 landmarks contained in a 100m x 100m region centered on TAG Site 1.
 log-typescript-Block-5A-Iterate-Landmarks-F3F1-Post05cmTilingANDgeometry
Achieve geometried state.
 Achieve residualed state.
 Achieve re-tiled state.
 Achieve sigma'ed state.

### Iterate
Repeat the following for the desired number of iterations.
Test F3F Procedures Block-5A - ITERATE LANDMARKS
 Iterate 358 landmarks contained in a 100m x 100m region centered on TAG Site 1.
 log-typescript-Block-5A-Iterate-Landmarks-F3F1-05cmIt01