# Test F3B - Number of Images
B Test Procedures
B Test Results
Goal: SPC derives much of its ability to remove error by using a large number of images, and as such, error becomes Gaussian noise. The purpose of the test is to measure the rate and magnitude of improvement with number of images.

## Test Set Up
Data:
- Approach, extra set of RC (Rotation Characterization) and closer set of RC
- Centered around the middle of TAG Site #1, -8.030 97.218
- Take the following images and add perturbed sets.
- Based upon F1b/DS results (Bennu2) with MAPLET EE0452 at 5cm resolution, -8.023 97.220.
- Test using 4, 7, 14, 70, and 140 images
- Uses the following images.
  Add displacements for this of x2, x10, x20
  - P601293751H3, P601372304H3, P601371742H3, P601372862F2, P601372869F2, P601293196F2, P601292636F2
Start: Preliminary Survey Model, TAG Site only, based on Shape 3.7.
Build:
- TAG site, near 0 latitude (for best evaluation).
- Create a 25x25m BIGMAP with MAPLETS at 5cm.
- Evaluate the center 20x20m to the truth model.
Sub-Tests
F3B-1	Use only four images: P601293751H3, P601372862F2, P601372869F2, P601293196F2
F3B-2	Use all seven images: P601293751H3, P601372304H3, P601371742H3, P601372862F2, P601372869F2, P601293196F2, P601292636F2
F3B-3	Use fourteen images, start with the base seven images and perturb them twice.
F3B-4	Use seventy images, start with the base seven images and perturb them ten times
F3B-5	Use one hundred and forty images, start with the base seven images and perturb them twenty times

Evaluate:
- Accuracy
- Relative Accuracy