# Translation Statistics

### By TC

## Description
This page is a users guide for transStats.py which is a python script that is meant for use in conjunction with batchCorrelation to yield some useful statistics about a region of interest in a shape model. This script expects an input in the form of locations.txt, which is one of the outputs of the batch correlation process.

## Usage
The syntax for this script is very simple, as it has one very specialized purpose. For general usage directions, running:

python transStarts.py -h
Will print out the usage header.

# USAGE: python transStats.py [-option] infile## -h Use this to print usage directions# to StdOut. (Prints this header)## -v Use this to only output current# version number and exit. By default# the version will be sent to StdOut# at the begining of each use.####################################################
A typical invocation of this script is as follows:

python transStats.py locations.txt
If you do not specify the input file, or any command line arguments, you will be prompted for a filename:

Input filename:

## Output
Once a correct input file is given, the calculated statistics are printed to the screen. After every successful invocation, the version number and input file will be printed to the screen for traceability.

transStats.py version: 1.1.1Input file: locations.txtMaximum: 42.3588285211Minimum: 41.3077804618Median: 41.748964396Average: 41.7606542577 dx: -41.4010377 dy: 5.43761855Standard Deviation: 0.280988725228Marginal Bound from Average: +/- 5Pass: 80.00% Marginal: 0.00% Fail: 20.00%Correlation < 0.5: 4 0.5-0.6: 5 0.6-0.7: 7 0.7-0.8: 4 0.8-0.9: 0 > 0.9: 0Pass: EE0115 EE0116 EE0117 EE0118 EE0119 EE0127 EE0128 EE0129 EE0130 EE0131 EE0139 EE0140 EE0141 EE0142 EE0143 EE0162 EE0163 EE0164 EE0165 EE0166Marginal:Fail: EE0151 EE0152 EE0153 EE0154 EE0155
The first thing that is done is the removal of outliers. Because of the nature of cross-correlation, and shape models, it is often the case that maplets will correlate to the wrong location. This can happen for many reasons, but generally this means the topography in that area is weak and needs further processing. So as of version 1.1.1 of transStats.py outliers are classified as such if their translation is 100 pixels or more than the average translation of all the maplets. This is a somewhat arbitrary criteria, but we felt it was very safe to assume that if a maplet is correlating that far away from the average deviation, it is obviously a fail. So far this has been very robust and not exclusive of any good data.
The outliers are now placed into the "Fail" category, and a new average is calculated. All of the statistics before the pass/marginal/fail percentages are calculated AFTER the removal of the outliers, and give a variety of useful information. It is good to see that the maximum, average, and median translation magnitudes are very close together. This means there is good agreement of the data.
After the statistics are calculated the data is split, once again, into pass and marginal categories. As of version 1.1.1, the bound for classifying a maplet as marginal is if it translated 5 or more pixels from the new average that was calculated after removal of outliers. Again, this is largely arbitrary, but for our applications so far, 5 makes for a good bound as these maplets should probably still be looked at further. Future versions may support user specified fail and/or marginal criteria.
The last thing that is done is the calculation of a correlation histogram that shows how many maplets fall into each correlation score bin. For our purposes, anything 0.6 and above is very good as we have seen that two resamplings of the same truth area give a correlation score of 0.833.