# make_scriptP
Category B	Version 3.0

## Description
The program generates the run script and .INN files required to iterate maplets using lithosP.

### Required Files
input file :
make_script.in - Text file containing a list of the landmarks to be processed, appended with the end-of-file identifier, 'END'.
seed file :
make_scriptP.seed - Test file containing the lithosP option commands for iterating each maplet.
processed files :
- INIT_LITHOS - make_scriptP reads the USRMX (maximum number of core processors) value.
- TESTFILES1/ - Directory in which to store copies of LMRK_DISPLAY.pgm (output by lithosP) for each landmark.
  /!\ lithosP requires a number of directories and files. Refer to lithosP for more information.

### Output Files
make_scriptP outputs :
- run.sh - Controlling run script for batch maplet iteration using parallel processing.
  - run script for each core processor:
    - run_script01.b
    - run_script02.b
    - etc ...
- .INN files - lithosP command seed file for each maplet.
- rem_script.b - Script for removal of temporary files (working directory clean-up).
run_script nn .b outputs :
.OOT files - standard output from lithosP for each landmark.]
processed files outputs :
- TESTFILES1/ - a copy of LMRK_DISPLAY.pgm (output by lithosP) is saved for each landmark;
- SUMFILES/ - S/C and camera information are updated by lithosP as image shifts are accepted. New landmarks and limb fits are added to the SUMFILEs;
- LMKFILES/ - LMKFILES are updated by lithosP.
- MAPFILES/ - MAPFILES are updated by lithosP.
  /!\ lithosP requires a number of directories and files. Refer to lithos for more information.

## User Warnings
{X} You must set the correct number of core processors for USRMX, a variable contained in INIT_LITHOS. Refer to that entry for further information.

## Using make_scriptP
For more information on iteration procedures, refer to the 'How-To': Standard_iteration.
Create Input Files
The make_script.in file lists the names for the landmarks that should be processed.
Here is a sample make_script.in file:
EE0001EE0002EE0003 etc...END
Be sure that the list is ordered by:
- highest-to-lowest maplet ground sample distance
- name (region identifier (e.g., FF ) + unique numeric identifier (e.g., 0001 ))
Also, be sure that there are no duplicate entries. You can use duplicates to generate the make_script.in file.
Here is a sample make_scriptP.seed file (see that entry for for further information):
# This script performs two maplet iterations in parallel mode. # It reinitializes slope and albedo.# It recomputes maplet overlaps.# It recomputes limb fits.# It recomputes central maplet vector.# Topography determination from slopes is conditioned by:# Initial topography, # Overlapping topography, # Shadowing, # Differential stereo, # Limb heghts. # Dataless area slopes are set from the shape model.## The script hides most of the screen output. In order to obtain the # full display replace H* by #H*.## Modified 2011_12_31. Header and comments added.# Modified 2014_02_26. Hide screen output added.#H*x.025## Initialize slope and albedo.#ayy## Begin first iteration.#040101n0yu040## Begin topo determination.#28 fill no data with shape slope2 condition with existing topo.017 condition with shadows.0251 condition with overlapping maps4 condition with limbs1, 2.5, 3 6 condition with differential stereoy0 begin integration.025150u102n0y101n0yu## Begin second iteration.#040101n0yu040## Begin topo determination.#282.017.025141, 2.5, 3 6y0.025150u102n0yH*101n0yH*u## Begin overlaps and limb fits.#oRECENTy1oRECENTn3y1, 3, 5 ## Central vector determination.#vRECENT qEND
Run make_scriptP
make_scriptP generates a .INN file for each maplet.
Here is a sample .INN file for maplet EE0001.INN :

01iEE0001H* x .025 0 40 etc ...
The first three lines of the .INN file supply a processor identifier (e.g., 01 ), and load the landmark in lithosP. The remainder of the .INN file lists a copy of the lithosP commands contained in make_scriptP.seed.
make_scriptP also generates the controller run script run.sh , which looks like this:

 chmod +x run_script01.b chmod +x run_script02.b etc ... cd SHAPEFILES chmod +w SHAPE.TXT cp SHAPE.TXT TSHP01.TXT cp SHAPE.TXT TSHP02.TXT etc ... chmod -w SHAPE.TXT cd .. ./run_script01.b & ./run_script02.b & etc ...
make_scriptP also generates the run_script01.b , run_script02.b etc. files, which look like this:
rm -f EE0001.OOT/usr/local/bin/LITHOSP < EE0001.INN > EE0001.OOTcp LMRK_DISPLAY01.pgm TESTFILES1/EE0001.pgmrm -f EE0007.OOT/usr/local/bin/LITHOSP < EE0007.INN > EE0007.OOTcp LMRK_DISPLAY01.pgm TESTFILES1/EE0007.pgmrm -f EE0013.OOT etc ...
Conduct Standard Iteration
Here is a sample command line for running run.sh :
sh run.sh
You can also run this in the background using this command line:
nohup sh run.sh &
The lithosP standard output for each image is captured in the .OOT files. The LMRKDISPLAY.pgm file output by lithosP is copied and saved in TESTFILES1/ once a landmark has been processed.
Quality Check Iterated Maplets
You must review the .OOT files to ascertain the success of the iteration process. You can detect problem landmarks using find_nofitP. Refer to that entry for more information.
Clean Working Directory
You can use rem_script.b to clean out the directory of make_scriptP working files once iteration is complete and you have quality checked the iterated maplets.
Here is a sample rem_script.b file:

rm -f *.INNrm -f *.OOTrm -f run_script*

(Compiled by DL)
CategoryPrograms