# make_scriptT.in

## Description
This support file is used by make_scriptT, the script-maker for tiling a bigmap or shape.

## Basic Tiling
Basic tiling involves tiling a bigmap which is located on the shape. For more details, refer to Basic_tiling.
Here is an annotated sample of a make_scriptT.in file used for basic tiling:

XXXXXX <- For maplet locations, reference to temporary file containing the tiling bigmapscripts/t11-10.seed <- Reference to the make_scriptT.seed file 50 50 <- bigmap pixel/line location for placement of the center of each new maplet 100 50 150 50 200 50 50 100 100 100 150 100 200 100 50 150 100 150 150 150 200 150 50 200 100 200 150 200 200 200END
XXXXXX - You must save the tiling bigmap to a temporary file for tiling using a command line like this:
cp MAPFILES/BGMAP1.MAP MAPFILES/XXXXXX.MAP
You then include the temporary filename as the first line of the file.
make_scriptT seed file - File containing the lithos commands for generating each new maplet. Refer to make_scriptT.seed for more information.
bigmap pixel/line locations - These are generated using the programs map_coverage and make_tilefile. Refer to those entries for details.

## Lat/Long Tiling
Lat/Long tiling involves directly tiling a shape model. For more details, refer to LatLon_tiling.
Here is an annotated sample make_scriptT.in file used for lat/long tiling:
LATLON <- For maplet locations, reference to shape modelSCRIPTS/XXX150.SEED <- Reference to the make_scriptT.seed file 00, 000 <- shape model lat/wlong for placement of the center of each new maplet 00, 012 00, 024 00, 036 00, 048 00, 060 00, 072 00, 084 ....-84, 315 90, 000-90, 000END
make_scriptT seed file - File containing the lithos commands for generating each new maplet. Refer to make_scriptT.seed for more information.

## Image Tiling
- The 1st line must be "IMAGES".
- The 2nd line is the script name
- Following lines are image name, sample and pixel
  - Image name must be char 1-12.
    Sample and pixel are after that with any fortran format (space or comma delimited)
- Ends with the statement "END"
- # symbol will cause that entry to be skipped
Here is an annotated sample make_scriptT.in file used for tiling an image:
IMAGES <- For maplet locations, reference to shape modelTIL_eekingLimbsInImage.seed <- Reference to the make_scriptT.seed fileD7175061248G 358 511 <- image name followed up pixel/line location D7175061210G 372 515D7175061210G 387 513D7175061210G 403 507 ....D7175061210G 566 887END

(Compiled by DL)
CategoryFiles CategorySupportFiles