# map_coverage
Category B	Version 3.0

## Description
This program generates coverage for a limited area (bigmap) of what has been tiled and processed. map_coverage produces a coverage_m.pgm file that shows areas on a bigmap that have been tiled at user specified resolutions. In the image, black means the area is not covered by a maplet while covered areas are bright. The brighter the area, the more maplets overlap that area.
Near the end of processing, there may be thousands of maplets. To speed things up, the routine will read in LMRKLISTO.TXT if it exists. This file speeds up map_coverage by telling the program exactly which maplets to show rather than having it search.

### Input Files
bigmap - a name provided in stdin

### Output Files
coverage_m.pgm - a regional map showing what has been tiled to the specified resolution

## Using map_coverage
Input the filename of a bigmap:

 ZN0204
Input the min and max resolution of tiles (maplets) to show:

 0,.001
Here is a sample output from map_coverage :

Figure 00: Example of map_coverage Output

 Compiled by KD
CategoryPrograms