# surface_imager
Category ?	Version ?

(!) This code was developed for the Mercator Project (LASER Program). The code uses Gaskell's basic infrastructure and data files.

## Description
surface_imager takes a bigmap and generates a surface image as if you are standing on (or near) the surface. It is designed to have a 100mm focal length lens and generate a 1024x1024 image.

## Input Files
none

## Input stdin
- Bigmap name
- Location of the point of view (x, y, z).
  X and Y are pixel positions within the map.
  Z is in meters above the surface.
- Direction that you are looking (azimuth and elevation - in degrees).
  Zero azimuth is looking due north.
  Zero elevation is looking at the horizon.
- Sun position (azimuth and elevation - in degrees).
  Zero azimuth has the Sun due north.
  90 elevation is the Sun straight up.
Here's a sample input:
1234561733 1393 1090, 060, 30 <- low sun angle

## Output
IMAGE.pgm - The output image.
Normally, it is 1024x1024 of the field of view (about 24 degrees square).

 CategoryPrograms CategoryMercator