# view_maps
What this program does (Makes an image of the map coverage)

### Requires - files
- geometry.in -- typically, this will be copied from geometry_01.in to geometry_08.in
- view_maps.in
- SHAPEFILES/SHAPE00.TXT -- This is a dumbed down version of the shape.
  It is used when you select the shapefile outline option (4/5/6)

### Input - stdin
Menu

   Running VIEW_MAPS 0. All maps 1. Maps with lmks or limbs 2. Maps with lmks 3. Maps with lmks, no albedo 4. All maps + shape outline 5. Maps with lmks or limbs + shape outline 6. Maps with lmks + shape outline
It works best to just select option 5.
This will build the object as well as put a thin line depicting the base shape (as defined by SHAPE00.txt)

### Output
view.jpg -- the image taken from one of the geometry.in stations.